## Slide 1
MRI SEQUENCES
A Comprehensive Guide for Clinical Radiology
Understanding T1, T2, FLAIR, DWI, GRE, STIR & More
Radiology / Medical Imaging Lecture Series
2026

## Slide 2
TABLE OF CONTENTS
01
MRI Physics Basics
How MRI signal is generated
02
T1-Weighted Imaging
Short TR, Short TE — anatomy & post-contrast
03
T2-Weighted Imaging
Long TR, Long TE — pathology detection
04
FLAIR Sequence
Fluid Attenuated Inversion Recovery
05
DWI & ADC
Diffusion Weighted Imaging
06
GRE / T2* Sequences
Gradient Echo & susceptibility
07
STIR Sequence
Short Tau Inversion Recovery — fat suppression
08
Special Sequences
MRA, MRS, Perfusion, fMRI & more
09
Clinical Applications
Choosing the right sequence

## Slide 3
01 MRI PHYSICS BASICS
How MRI Signal is Generated
• Hydrogen protons (¹H) align with external magnetic field (B₀)
• Radiofrequency (RF) pulse tips protons out of alignment
• Protons precess at Larmor frequency: ω = γ × B₀
• Signal detected as protons relax back to equilibrium
• Two relaxation processes: T1 (longitudinal) & T2 (transverse)
Key Parameters
• TR (Repetition Time) — time between RF pulses (ms)
• TE (Echo Time) — time between RF pulse and signal reading
• TI (Inversion Time) — used in inversion recovery sequences
• Flip Angle — degree of magnetization tipping
• Field Strength: 1.5T (standard) vs 3T (high-res)
⚡ Key Concept
T1 relaxation = longitudinal recovery (spin-lattice). T2 relaxation = transverse decay (spin-spin). Sequence contrast depends on TR and TE choices relative to tissue T1/T2 values.

## Slide 4
02 T1-WEIGHTED IMAGING
Parameters
• Short TR: 400–600 ms
• Short TE: 10–30 ms
• Emphasizes T1 differences between tissues
Tissue Appearance
• FAT → Bright (high signal) ✨
• FLUID (CSF, urine) → Dark (low signal)
• MUSCLE → Intermediate
• CORTICAL BONE → Dark
• GREY MATTER → Slightly darker than white matter
• WHITE MATTER → Brighter than grey matter
Clinical Uses
• Anatomy — excellent soft tissue detail
• Post-gadolinium contrast enhancement
• Fat detection (lipoma, dermoid)
• Hemorrhage (subacute — methemoglobin bright)
• Liver lesions characterization
• Pituitary gland imaging
• Bone marrow assessment
🔶 T1 BRIGHT (Short T1)
Fat | Subacute blood (Met-Hb) | Gadolinium contrast | Proteinaceous fluid | Melanin | Calcium (sometimes) | Lipid-containing lesions
🔷 T1 DARK (Long T1)
Free fluid (CSF, edema, cysts) | Acute blood | Air | Cortical bone | Most pathology (tumors, infarcts)

## Slide 5
03 T2-WEIGHTED IMAGING
Parameters
• Long TR: 2000–4000 ms
• Long TE: 80–120 ms
• Emphasizes T2 differences — fluid appears bright
• Called the 'pathology sequence'
Tissue Appearance
• FLUID (CSF, edema) → Bright ✨
• FAT → Intermediate-bright
• MUSCLE → Dark
• CORTICAL BONE → Dark
• GREY MATTER → Brighter than white matter
• WHITE MATTER → Darker than grey matter
• PATHOLOGY → Mostly bright (edema, tumors)
Clinical Uses
• Edema detection (brain, spine, joints)
• Joint fluid & cartilage evaluation
• Spinal cord pathology
• Liver & kidney lesions
• Pelvic organs (uterus, prostate)
• Breast MRI
• Inflammation & infection
• CSF flow studies
T1 vs T2 — Quick Comparison
Tissue
T1 Signal
T2 Signal
Fat
Bright
Bright
Free Fluid
Dark
Bright
Muscle
Intermediate
Dark
Air/Bone
Dark
Dark
Edema
Dark
Bright
Subacute Blood
Bright
Bright

## Slide 6
04 FLAIR — Fluid Attenuated Inversion Recovery
How FLAIR Works
• Inversion Recovery sequence with long TI (~2000 ms at 1.5T)
• TI chosen to null free water/CSF signal
• CSF appears BLACK (suppressed)
• Periventricular & cortical lesions become visible
• Lesions near CSF spaces that are hidden on T2 become conspicuous
Key Clinical Applications
• Multiple Sclerosis (MS) plaques — periventricular
• Subarachnoid hemorrhage (SAH) — blood bright in CSF spaces
• Cortical contusions & traumatic brain injury
• Encephalitis (herpes, autoimmune)
• Leptomeningeal disease / carcinomatosis
• Early ischemic stroke changes
• Cortical dysplasia
⚡ FLAIR vs T2 — When to use which?
T2: Best overall pathology detection — fluid AND lesions both bright FLAIR: Best for PERIVENTRICULAR and CORTICAL lesions — nulls CSF so adjacent lesions stand out Rule: Always review T2 and FLAIR together for brain pathology (especially MS, SAH, encephalitis)

## Slide 7
05 DWI & ADC — Diffusion Weighted Imaging
Principle of DWI
• Measures Brownian motion of water molecules
• Applies gradient pulses to sensitize motion
• b-value controls diffusion weighting (b=0, 500, 1000 s/mm²)
• RESTRICTED diffusion → Bright on DWI
• FREE diffusion → Dark on DWI
• T2 shine-through can mimic restriction — always check ADC!
ADC Map Interpretation
• ADC = Apparent Diffusion Coefficient map
• Mathematically derived from DWI
• TRUE restriction: DWI bright + ADC dark (low ADC)
• T2 shine-through: DWI bright + ADC bright
• Low ADC value < 0.8 × 10⁻³ mm²/s = significant restriction
• High ADC = free diffusion / vasogenic edema
🏥 Clinical Applications of DWI
• Acute ischemic stroke (cytotoxic edema — bright within minutes)
• Abscess (restricted pus — bright center, helps vs necrotic tumor)
• Epidermoid cyst vs arachnoid cyst
• Diffuse axonal injury (DAI)
• Creutzfeldt-Jakob disease (CJD) — cortical ribboning
• Lymphoma (hypercellular — restricted)
• Cholesteatoma
• Prostate & rectal cancer staging

## Slide 8
06 GRE / T2* — Gradient Echo & Susceptibility
GRE Principle
• Uses gradient reversal instead of 180° RF refocusing pulse
• Does NOT cancel field inhomogeneity effects
• Susceptible to T2* (T2-star) decay
• Much faster than spin echo sequences
• Flip angle < 90° (typically 15–60°)
• Small flip angle → more T2* weighting
Susceptibility Artifacts
• Paramagnetic substances cause local field distortion
• Blood products (deoxyhemoglobin, hemosiderin) → DARK
• Air-tissue interfaces → signal loss / blooming
• Metal implants → severe distortion
• 'Blooming artifact' — lesions appear larger than actual
• SWI (Susceptibility Weighted Imaging) = enhanced T2*
Clinical Uses
• Microbleeds (hypertensive, CAA, DAI)
• Cavernous malformations
• Hemorrhagic transformation of infarct
• Iron deposition (basal ganglia disorders)
• Calcifications (T2* dark)
• Venous thrombosis (SWI)
• Tumor blood products
• Functional MRI (fMRI) — BOLD technique
Hemorrhage on MRI — Signal Evolution Over Time
Stage
Content
T1
T2
GRE
Hyperacute (<24h)
Oxy-Hb
Dark
Bright
Iso/Dark
Acute (1–3d)
Deoxy-Hb
Dark
Dark
Dark
Early Subacute (3–7d)
Met-Hb (intra)
Bright
Dark
Dark
Late Subacute (1–2wk)
Met-Hb (extra)
Bright
Bright
Dark
Chronic (>2wk)
Hemosiderin
Dark
Dark
Very Dark

## Slide 9
07 STIR — Short Tau Inversion Recovery
How STIR Works
• Inversion Recovery sequence with SHORT TI
• TI chosen to null FAT signal (~150ms at 1.5T, ~210ms at 3T)
• Fat appears BLACK (suppressed)
• Fluid/edema remains BRIGHT
• Additive effect: T1 + T2 weighting → very sensitive to water
• Works at any field strength (unlike spectral fat sat)
Clinical Applications
• Bone marrow edema (fractures, osteomyelitis, metastases)
• Soft tissue edema & inflammation
• Muscle injuries & tears
• Brachial plexus imaging
• Spinal cord & nerve root pathology
• Lymph node evaluation
• Body MRI where spectral fat sat unreliable
• Pediatric imaging
STIR vs Spectral Fat Saturation (Fat Sat) — Key Differences
Feature
STIR
Spectral Fat Sat
Mechanism
Inversion Recovery (TI)
Chemical shift saturation pulse
Field strength
Works at all field strengths
Best at high field (1.5T, 3T)
Uniformity
Uniform fat suppression
Inhomogeneous at air-tissue interfaces
SNR
Lower SNR
Higher SNR
Contrast injection
Cannot be used (nulls Gd)
Safe with contrast

## Slide 10
08 SPECIAL SEQUENCES
MRA MR Angiography
• TOF (Time of Flight) — flow-related enhancement
• Phase Contrast — velocity encoding
• CE-MRA — contrast enhanced
• Evaluates arteries & veins non-invasively
MRS MR Spectroscopy
• Measures brain metabolite peaks
• NAA (neurons), Cho (membranes),
• Cr (reference), Lac (anaerobic), Lip
• Tumor vs radiation necrosis
Perfusion MRI
• DSC (Dynamic Susceptibility Contrast)
• ASL (Arterial Spin Labeling) — no contrast
• Maps CBF, CBV, MTT, TTP
• Stroke, tumor grading, seizures
fMRI Functional MRI
• BOLD technique (Blood Oxygen Level Dependent)
• Maps brain activation patterns
• Pre-surgical planning
• Eloquent cortex mapping
MRCP
• MR Cholangiopancreatography
• Heavy T2 — fluid bright
• Bile ducts, pancreatic duct
• No contrast, no radiation
DTI Diffusion Tensor
• Tracks white matter tracts
• Fractional Anisotropy (FA) maps
• Pre-surgical tractography
• TBI assessment
Dixon / Fat-Water
• Separates fat & water images
• In-phase / Out-of-phase
• PDFF (fat quantification)
• Liver steatosis grading
Cine MRI / EPI
• Cardiac gated sequences
• Real-time cardiac function
• EPI — fast single-shot
• fMRI & perfusion base

## Slide 11
09 CLINICAL APPLICATIONS — Choosing the Right Sequence
Acute Stroke
DWI + ADC (first line) FLAIR (after 6h) MRA for vessel occlusion T2* / SWI for hemorrhage
Brain Tumor
T1 + T1 post-Gad (enhancement) T2 / FLAIR (extent, edema) DWI (cellularity) MRS (metabolites) Perfusion (grading)
Multiple Sclerosis
FLAIR (periventricular plaques) T2 (overall lesion load) T1 (black holes = axonal loss) Spinal T2 (cord lesions)
Spine Pathology
T1 (anatomy, bone marrow) T2 (disc, cord, fluid) STIR (edema, metastases) DWI (cord, vertebral lesion)
Knee / Joint
PD Fat Sat / T2 Fat Sat (menisci, cartilage) T1 (anatomy) GRE (cartilage volume) STIR (bone bruise, edema)
Liver Lesion
T1 in/out phase (fat, iron) T2 (cyst, hemangioma) DWI (malignancy) T1 dynamic post-Gad Dixon fat quantification

## Slide 12
QUICK REFERENCE — MRI Sequences Summary
Sequence
TR
TE
Fat
Fluid
Key Use
T1
Short
Short
Bright
Dark
Anatomy, Post-Gad, Fat
T2
Long
Long
Bright
Bright
Pathology, Edema, Fluid
FLAIR
Long
Long
Bright
Dark (nulled)
Periventricular lesions, SAH
DWI
—
Short
—
—
Acute stroke, Abscess, Tumor
GRE/T2*
Short
Short
Bright
Dark
Hemorrhage, Iron, Calcification
STIR
Long
Long
Dark (nulled)
Bright
Bone marrow edema, Soft tissue
SWI
Long
Long
—
—
Microbleeds, Veins, Calcium
MRCP
Very Long
Very Long
Dark
Very Bright
Bile/Pancreatic ducts
MRS
—
—
—
—
Tumor metabolites, Necrosis